## Slide 2: Preparing a Benefit-Cost Analysis for INFRA Grants
Office of the Assistant Secretary for Transportation Policy

## Slide 3: What is BCA?
Benefit-cost analysis (BCA) is a systematic process for identifying, quantifying, and comparing expected economic benefits and costs of a proposed infrastructure project.

## Slide 4: Why do we do BCA?
Provides a useful benchmark from which to evaluate and compare potential transportation investments
Adds a degree of rigor to the project evaluation process

## Slide 5: BCA and INFRA
All project sponsors should submit a benefit-cost analysis (BCA) as part of their INFRA grant application
Use of the BCA in INFRA
  Evaluation of the Economic Vitality selection criterion
  Assignment of a Freight Benefits rating
  Assessment of project cost-effectiveness

## Slide 6: USDOT BCA Review
USDOT economists will review the applicant’s BCA
  Examine key assumptions
  Correct for any technical errors
  Perform sensitivity analysis on key inputs
  Consider any unquantified benefits

## Slide 7: Economic Vitality
USDOT considers the relative magnitude of estimated project benefits and costs
Assign projects to one of four benefit-cost ratio ranges
  BCR > 3.0
  BCR 1.5 - 3.0
  BCR 1.0 - 1.5
  BCR < 1.0
Also assign a confidence rating to the assessment (high, medium, low)

## Slide 8: Freight Rating
USDOT considers the significance of freight benefits for a project
Assign one of three ratings, based on the share of total quantifiable benefits that are attributable to impacts on freight movement
  Substantial freight benefits: ≥ 20%
  Moderate freight benefits: 5-20%
  Incidental freight benefits: < 5%

## Slide 9: INFRA Cost Effectiveness Requirements
Large Projects
  USDOT must determine that the project will be cost effective in order for it to be selected
Small Projects
  USDOT must consider project cost-effectiveness in making selections
Cost-effectiveness determinations based on results of the BCA
  Projects must be found to have estimated benefits that are reasonably likely to exceed costs in order to be considered cost effective

## Slide 10: USDOT BCA Guidance
Covers all USDOT discretionary grant programs
Updated February 2021
Available at https://www.transportation.gov/office-policy/transportation-policy/benefit-cost-analysis-guidance

## Slide 11: What’s New?
Updated monetization values
Additional guidance on valuing reductions in emissions (including CO2)
Additional guidance on benefits from agglomeration economies and state of good repair projects

## Slide 12: Transparent & Reproducible Analysis
BCAs should provide enough information for a reviewer to follow the logic and reproduce the results
  Spreadsheet or database files showing the calculations
  Technical memos describing the analysis and documenting sources of information used (assumptions and inputs)
  Present annual benefit & cost streams by type (not just summary output)

## Slide 13: Baselines
Should measure costs and benefits of a proposed project against a baseline alternative (“base” or “no build”)
“Do’s”
  Factor in any projected changes (e.g., increased traffic volumes) that would occur even in the absence of the requested project
  Factor in ongoing routine maintenance
  Consider full long-term impacts of no build (e.g. bridge closure/posting)
  Explain and provide support for the chosen baseline
“Don’t’s”
  Assume that the same (or similar) improvement will be implemented later
  Use unrealistic assumptions about alternative traffic flows

## Slide 14: Demand Forecasts
Most benefit estimates depend on ridership or usage estimates
Provide supporting info on forecasts
  Geographic scope, assumptions, data sources, methodology
Provide forecasts for intermediate years
  Or at least interpolate—don’t apply forecast year impacts to interim years
Exercise caution about long-term growth assumptions
  Consider underlying capacity limits of the facility

## Slide 15: Analysis Period
Should cover both initial development and construction and a subsequent operational period
Generally tied to the expected service life of the improvement or asset
  I.e., the number of years until you would anticipate having to take the same action again
  Lesser improvements should have shorter service lives
Avoid excessively long analysis periods (over 30 years of operations)
  Use residual value to cover out-years of remaining service life for long-lived assets
  Recommend 20 years maximum for capacity expansion

## Slide 16: Inflation and Discounting
Inflation Adjustments
  Recommend using a 2019 base year for all cost and benefit data
  Index values for the GDP Deflator included in the BCA guidance
Discounting
  Use a 7% discount rate for all benefits and costs (except CO2)

## Slide 17: Scope of the Analysis
Project scope included in estimated costs and benefits must match
  Don’t claim benefits from an entire project, but only count costs from the grant-funded portion
Scope should cover a project that has independent utility
  May need to incorporate costs for related investments necessary to achieve the projected benefits
Project elements with independent utility should be individually evaluated in the BCA
  BCA evaluation will cover both independent elements and the submitted project as a whole

## Slide 18: Benefits
Should be presented on an annual basis
  Don’t assume constant annual benefits without a good reason to do so
Negative outcomes should be counted as “disbenefits”
  E.g., work zone impacts
Avoid double-counting benefits

## Slide 19: Travel Time Savings
Recommended values found in BCA Guidance
  See footnotes for discussion of non-vehicle time, long-distance travel, business travel
Consider vehicle occupancy where appropriate
  Local/facility-specific values preferred
  National-level values provided in BCA Guidance
If valuing travel time reliability:
  Carefully document methodology and tools used
  Show how valuation parameters are distinct from general travel time savings

## Slide 20: Operating Cost Savings
Avoid double counting operating savings and other impacts
  E.g., truck travel time savings, fuel consumption reductions
Localized, specific data preferred
  Standard per-mile values for light duty vehicles and commercial trucks provided in DOT BCA Guidance

## Slide 21: Safety Benefits
Typically associated with reducing fatalities, injuries, and property damage
Projected improvements in safety outcomes should be explained and documented
  Justify assumptions about expected reductions in crashes, injuries, and/or fatalities (and document any CMF used)
  Show clear linkage between project and improved outcomes
  Use facility-specific data history for baseline where possible
Crash-related injury and fatality data may be available in different forms
  MAIS/KABCO injury scales
  Fatal/Injury crashes vs. fatalities/injuries
  BCA Guidance provides values covering all of these

## Slide 22: Emissions Reduction Benefits
For infrastructure improvements, emissions reductions will typically be a function of reduced fuel consumption
Recommended year by year unit values for CO2, SO2, NOx, and PM2.5 found in BCA guidance
  Be careful about the measurement units being applied
Reductions in CO2 emissions should be discounted at 3 percent, while all others should be discounted at 7 percent

## Slide 23: Benefits to Existing and Additional Users
Primary benefits typically experienced directly by users of the improved facility
Includes both “existing” users (under baseline) and “additional” users attracted to the facility as a result of the improvement
  Standard practice in BCA would value benefits to additional users less than those for existing users (see BCA guidance)

## Slide 24: Modal Diversion
Projected magnitude
  Should be based on careful analysis of the market and potential for diversion from other modes that might be attributable to the project
Benefits estimates should not be based on comparing user costs of “old” and “new” mode
  Would be reflected in benefits to additional users
Reductions in external costs would be relevant
  E.g., emissions costs, pavement damage
If using 1997 HCAS values…
  Don’t apply urban values to rural truck travel
  Should net out highway user fees paid by trucks from marginal pavement damage costs

## Slide 25: Other Benefits
Agglomeration Economies
State of Good Repair
Resilience
  Consider expected frequency of events and their consequences
Noise Reduction
Emergency Response
  FEMA methodology for fire and ambulance services
Quality of Life
Property Value Increases
  Is a measure rather than a benefit—avoid double-counting

## Slide 26: Unquantified Benefits
Should quantify magnitudes/timing of the impacts wherever possible
Should clearly link specific project outcomes to any claimed unquantified benefits

## Slide 27: Capital Costs
Include all costs of implementing the project
  E.g., design, ROW acquisition, construction
  Regardless of funding source
  Include previously incurred costs
Three forms of capital costs
  Nominal dollars (project budget)
  Real dollars (base year)
  Discounted Real dollars (use in BCA)

## Slide 28: Maintenance Costs
Net maintenance costs may be positive or negative
  New facilities would incur ongoing maintenance costs over the life of the project
  Rehabilitated/reconstructed facilities may result in net savings in maintenance costs between the build/no-build

## Slide 29: Residual Value
For assets with remaining service life at the end of the analysis period, may calculate a “residual value” for the project
Simple approach: assume linear depreciation
Be sure to properly apply discounting

## Slide 30: Comparing Benefits to Costs
Net Present Value (Benefits – Costs)
Benefit-Cost Ratio (Benefits / Costs)
  Denominator should only include capital costs (i.e., net maintenance costs and residual value should be in the numerator)

## Slide 31: Other Types of Economic Analysis
Examples
  Economic Impact Analysis
  Financial Impacts
  Distributional Effects
Issues
  Use different approaches and answer different questions than does BCA
  Do not represent additional benefits to include in BCA

## Slide 32: INFRA Grants
For additional INFRA information and how to apply: www.transportation.gov/buildamerica/INFRAgrants
For technical questions, please email: INFRAgrants@dot.gov.

## Slide 33
Questions?

## Slide 34: Hypothetical BCA Example
Proposed Project: Replace a deteriorating bridge.
Project Cost: $2.5 million
2020
AADT: 1,000 Cars per Day (Source: Traffic Count)
Avg. Speed: 45 mph (State DOT database)

## Slide 35: Hypothetical BCA Example
No-Build Scenario: Bridge closes in 2025 and traffic is detoured
(2.6-mile route).

## Slide 36: Hypothetical BCA Example
Build Scenario: Bridge Remains open to traffic
(1.0-mile route).
No-Build Scenario: Bridge closes in 2025 and traffic is detoured
(2.6-mile route).

## Slide 37: Hypothetical BCA Example
Build Scenario: Bridge Remains open to traffic
(1.0-mile route).
No-Build Scenario: Bridge closes in 2025 and traffic is detoured
(2.6-mile route).
No-Build Scenario detour is 1.6 miles longer than Build Scenario route.

## Slide 38: Approach
We want to compare the state of the world with and without the proposed project improvement.
  No-Build Scenario: Bridge closes in 2025, traffic detours 2.6 miles.
  Build Scenario: Bridge remains open, existing route is 1.0 miles.
The expected major benefit categories in this case would be vehicle operating cost savings and travel time savings for mitigating 1.6-miles of additional travel, starting in 2025.

## Slide 39: Vehicle Operating Cost Savings
For simplicity, let’s assume no heavy trucks and no traffic growth.
Annual Vehicle Operating Cost Savings*
Incremental Detour
AADT
Vehicle Operating Cost Per Mile
Annualization Factor
=
x
x
x
*Undiscounted.

## Slide 40: Vehicle Operating Cost Savings
For simplicity, let’s assume no heavy trucks and no traffic growth.
Annual Vehicle Operating Cost Savings*
Incremental Detour
AADT
Vehicle Operating Cost Per Mile
Annualization Factor
=
x
x
x
Annual Vehicle Operating Cost Savings*
=
*Undiscounted.

## Slide 41: Vehicle Operating Cost Savings
For simplicity, let’s assume no heavy trucks and no traffic growth.
Annual Vehicle Operating Cost Savings*
Incremental Detour
AADT
Vehicle Operating Cost Per Mile
Annualization Factor
=
x
x
x
Annual Vehicle Operating Cost Savings*
1.6 Miles
=
*Undiscounted.
No-Build Scenario route: 2.6 miles
Build Scenario route: 1.0 miles

## Slide 42: Vehicle Operating Cost Savings
For simplicity, let’s assume no heavy trucks and no traffic growth.
Annual Vehicle Operating Cost Savings*
Incremental Detour
AADT
Vehicle Operating Cost Per Mile
Annualization Factor
=
x
x
x
Annual Vehicle Operating Cost Savings*
1.6 Miles
1,000
=
x
*Undiscounted.
Recent traffic count

## Slide 43: Vehicle Operating Cost Savings
For simplicity, let’s assume no heavy trucks and no traffic growth.
Annual Vehicle Operating Cost Savings*
Incremental Detour
AADT
Vehicle Operating Cost Per Mile
Annualization Factor
=
x
x
x
Annual Vehicle Operating Cost Savings*
1.6 Miles
1,000
$0.43
=
x
x
*Undiscounted.
USDOT BCA Guidance
(Appendix A)

## Slide 44: Vehicle Operating Cost Savings
For simplicity, let’s assume no heavy trucks and no traffic growth.
Annual Vehicle Operating Cost Savings*
Incremental Detour
AADT
Vehicle Operating Cost Per Mile
Annualization Factor
=
x
x
x
Annual Vehicle Operating Cost Savings*
1.6 Miles
1,000
$0.43
365
=
x
x
x
*Undiscounted.
We expect this project to have an impact each day (not just weekdays, for example).

## Slide 45: Vehicle Operating Cost Savings
For simplicity, let’s assume no heavy trucks and no traffic growth.
Annual Vehicle Operating Cost Savings*
Incremental Detour
AADT
Vehicle Operating Cost Per Mile
Annualization Factor
=
x
x
x
Annual Vehicle Operating Cost Savings*
1.6 Miles
1,000
$0.43
365
=
x
x
x
=
$251,120 Per Year
*Undiscounted.

## Slide 46: Travel Time Savings
For simplicity, let’s assume no heavy trucks, an average speed of 45 mph, and no traffic growth.
Annual Vehicle Travel Time Savings*
Marginal Detour Time
AADT
Hourly Value of Time
Annualization Factor
=
x
x
x
x
Vehicle Occupancy
*Undiscounted.

## Slide 47: Travel Time Savings
For simplicity, let’s assume no heavy trucks, an average speed of 45 mph, and no traffic growth.
Annual Vehicle Travel Time Savings*
Marginal Detour Time
AADT
Hourly Value of Time
Annualization Factor
=
x
x
x
x
Vehicle Occupancy
Annual Vehicle Travel Time Savings*
1.6 Miles
45 mph
=
*Undiscounted.
No-Build Scenario route: 2.6 miles
Build Scenario route: 1.0 miles
Speed: Observed average speed on both routes

## Slide 48: Travel Time Savings
For simplicity, let’s assume no heavy trucks, an average speed of 45 mph, and no traffic growth.
Annual Vehicle Travel Time Savings*
Marginal Detour Time
AADT
Hourly Value of Time
Annualization Factor
=
x
x
x
x
Vehicle Occupancy
Annual Vehicle Travel Time Savings*
1.6 Miles
45 mph
1,000
=
x
x
*Undiscounted.
Recent traffic count

## Slide 49: Travel Time Savings
For simplicity, let’s assume no heavy trucks, an average speed of 45 mph, and no traffic growth.
Annual Vehicle Travel Time Savings*
Marginal Detour Time
AADT
Hourly Value of Time
Annualization Factor
=
x
x
x
x
Vehicle Occupancy
Annual Vehicle Travel Time Savings*
1.6 Miles
45 mph
1,000
$17.90
=
x
x
*Undiscounted.
USDOT BCA Guidance
(Appendix A)

## Slide 50: Travel Time Savings
For simplicity, let’s assume no heavy trucks, an average speed of 45 mph, and no traffic growth.
Annual Vehicle Travel Time Savings*
Marginal Detour Time
AADT
Hourly Value of Time
Annualization Factor
=
x
x
x
x
Vehicle Occupancy
Annual Vehicle Travel Time Savings*
1.6 Miles
45 mph
1,000
$17.90
=
x
x
x
1.67
*Undiscounted.
USDOT BCA Guidance
(Appendix A)

## Slide 51: Travel Time Savings
For simplicity, let’s assume no heavy trucks, an average speed of 45 mph, and no traffic growth.
Annual Vehicle Travel Time Savings*
Marginal Detour Time
AADT
Hourly Value of Time
Annualization Factor
=
x
x
x
x
Vehicle Occupancy
Annual Vehicle Travel Time Savings*
1.6 Miles
45 mph
1,000
$17.90
365
=
x
x
x
x
1.67
*Undiscounted.
We expect this project to have an impact each day (not just weekdays, for example).

## Slide 52: Travel Time Savings
For simplicity, let’s assume no heavy trucks, an average speed of 45 mph, and no traffic growth.
Annual Vehicle Travel Time Savings*
Marginal Detour Time
AADT
Hourly Value of Time
Annualization Factor
=
x
x
x
x
Vehicle Occupancy
Annual Vehicle Travel Time Savings*
1.6 Miles
45 mph
1,000
$17.90
365
=
x
x
x
x
1.67
=
$387,945 Per Year
*Undiscounted.

## Slide 53: Hypothetical BCA Example
Assume construction in 2022, ten years of project operations, and no difference in bridge maintenance costs between the scenarios.
Year | Capital Cost |  | Vehicle Operating Cost Savings | Vehicle Travel Time Savings | 
2022 | $2,500,000 |  | $0 | $0 | 
2023 | $0 |  | $0 | $0 | 
2024 | $0 |  | $0 | $0 | 
2025 | $0 |  | $251,120 | $387,945 | 
2026 | $0 |  | $251,120 | $387,945 | 
2027 | $0 |  | $251,120 | $387,945 | 
2028 | $0 |  | $251,120 | $387,945 | 
2029 | $0 |  | $251,120 | $387,945 | 
2030 | $0 |  | $251,120 | $387,945 | 
2031 | $0 |  | $251,120 | $387,945 | 
2032 | $0 |  | $251,120 | $387,945 | 
Bridge Closure Year (No-Build Scenario)

## Slide 54: Hypothetical BCA Example
Next we discount costs and benefits using a 7% discount rate.
Year | Capital Cost | Discounted Costs | Vehicle Operating Cost Savings | Vehicle Travel Time Savings | Discounted Benefits
2022 | $2,500,000 | $2,336,449 | $0 | $0 | $0
2023 | $0 | $0 | $0 | $0 | $0
2024 | $0 | $0 | $0 | $0 | $0
2025 | $0 | $0 | $251,120 | $387,945 | $487,539
2026 | $0 | $0 | $251,120 | $387,945 | $455,644
2027 | $0 | $0 | $251,120 | $387,945 | $425,836
2028 | $0 | $0 | $251,120 | $387,945 | $397,977
2029 | $0 | $0 | $251,120 | $387,945 | $371,941
2030 | $0 | $0 | $251,120 | $387,945 | $347,609
2031 | $0 | $0 | $251,120 | $387,945 | $324,868
2032 | $0 | $0 | $251,120 | $387,945 | $303,615
Discounted Value = Future Year Value / (1+Discount Rate)^(Future Year - Base Discounting Year)
$2,500,000 / (1+0.07)^(2022-2021)
(251,120+387,945) / (1+0.07)^(2025-2021)
(251,120+387,945) / (1+0.07)^(2032-2021)

## Slide 55: Hypothetical BCA Example
Next we sum the discounted benefits and costs to get total discounted benefits and total discounted costs.
Year | Capital Cost | Discounted Costs | Vehicle Operating Cost Savings | Vehicle Travel Time Savings | Discounted Benefits
2022 | $2,500,000 | $2,336,449 | $0 | $0 | $0
2023 | $0 | $0 | $0 | $0 | $0
2024 | $0 | $0 | $0 | $0 | $0
2025 | $0 | $0 | $251,120 | $387,945 | $487,539
2026 | $0 | $0 | $251,120 | $387,945 | $455,644
2027 | $0 | $0 | $251,120 | $387,945 | $425,836
2028 | $0 | $0 | $251,120 | $387,945 | $397,977
2029 | $0 | $0 | $251,120 | $387,945 | $371,941
2030 | $0 | $0 | $251,120 | $387,945 | $347,609
2031 | $0 | $0 | $251,120 | $387,945 | $324,868
2032 | $0 | $0 | $251,120 | $387,945 | $303,615
TOTAL |  | $2,336,449 |  |  | $3,115,030

## Slide 56: Results – The NPV and BCR
Lastly, we calculate the project’s net present value (NPV) and benefit-cost ratio (BCR).
Net Present Value (NPV)
Benefit-Cost Ratio (BCR)
=
=
Total Discounted Benefits
Total Discounted Costs
Total Discounted Benefits
Total Discounted Costs
-
=
=
$3,115,030
-
$2,336,449
=
$778,582
$3,115,030
$2,336,449
=
1.3

## Slide 57
Questions?