## Slide 1: The U.S. Department Of Transportation
Intelligent Transportation Systems Joint Program Office
Preserving the 5.9GHz Safety Band For Transportation

## Slide 2: To Be Discussed Today:
Vehicle-to-Everything (V2X) technology is direct, device-to-device wireless messaging between vehicles, infrastructure and mobile devices—and uses 75 MHz of spectrum located at 5.9 GHz (termed the Safety Band) to support safety communications.
V2X technology enables game-changing advancements in transportation safety, system efficiency, and mobility.
The Safety Band is being utilized today—with substantial V2X deployments in 25 States—totaling over $1.5 billion in taxpayer funded investments—and more deployments are in the planning stage.
The proposed FCC NPRM reduces capacity in the Safety Band by 60%—which would limit the full potential of V2X technology to support innovative advancements in safety, system efficiency, and mobility.

## Slide 3: The Safety Band is 75 MHz of spectrum that supports “vehicle-to-everything” (V2X) wireless communications
Low Frequency
High Frequency
3 kHz
300 kHz
3 MHz
30 MHz
300
MHz
3GHz
30 GHz
The “Safety Band” is a 75MHz slice of spectrum located at 5.9 GHz

## Slide 4: History of 5.9 GHz Safety Band
In 1999, the Federal Communications Commission (FCC) allocated the section of wireless spectrum at 5.850-5.925 GHz for intelligent transportation systems (ITS) services.
Since then, U.S. DOT has worked with industry and the public sector to develop, evaluate, and deploy new cooperative technologies, equipment, and applications known as connected vehicle technologies, on this dedicated band. The technologies now reliant on the Safety Band include vehicle-to-vehicle (V2V), vehicle-to-infrastructure (V2I), and vehicle-to-everything (V2X) communications.

## Slide 5: But what is V2X ?
Vehicles can communicate directly
  with each other (vehicle-to-vehicle, V2V)
  with roadside infrastructure— (vehicle-to-infrastructure, V2I)
  and with portable devices such as those used by pedestrians (vehicle-to-pedestrian, V2P).
Direct communications between devices (no cell tower needed)

## Slide 6: Such direct communications offers opportunities for game-changing enhancements in vehicle safety and mobility. Examples:
  V2V: Messages are broadcast from each vehicle at a rapid rate (10 times per second!) and receiving vehicles use the information to predict potential collisions and warn the driver to take action.
  V2I: At the roadside, such technology can be used to wirelessly notify drivers/vehicles of traffic signal information; work zone locations; lane closures; and other roadway anomalies to both enhance safety and reduce congestion.

## Slide 7: And in the near future, vehicles with automated driving systems (ADS) may also leverage V2X. Examples:
  Commercial Vehicle Platooning
  Coordinated Intersection Movement Assist
  Notify ADS vehicles of approaching police and emergency vehicles
  Send wireless notifications of traffic signal and other roadside messages to enhance situational awareness for automated vehicles
  And other new and innovative features and applications

## Slide 8
The Safety Band is in use today
5.850 GHz |  |  |  |  |  | 5.925 GHz | 
 |  |  |  |  |  | CH 183 | 
 |  | CH 175 |  |  | CH 181 |  | 
5850-5855 reserve 5 MHz | CH 172 Service 10 MHz | CH 174 Service 10 MHz | CH 176 Service 10 MHz | CH 178 Service 10 MHz | CH 180 Service 10 MHz | CH 182 Service 10 MHz | CH 184 Service 10 MHz
WAVE
RSA
BSMs
SCMS
SPaT/MAP
Platooning
AVs
Red Light Viol
Curve Speed
V2 Pedestrian
Probe
V2V/V2I BSMs
SPaT/MAP
HMI
SCMS
Personal Safety
OTA Updates
Signal Request
Red Light Viol
Curve Speed
V2 Pedestrian
Probe
Public Safety
Signal Preemption
Signal Request
Vehicle Detected

## Slide 10: V2X is being deployed by State and local governments throughout the United States
There are currently 123 planned or operational connected vehicle deployment locations in the U.S., all of which use the Safety Band.
More than 18,000 vehicles are deployed with aftermarket V2X communications devices.
Over 6,000 infrastructure V2X devices have been installed at the roadside in 25 states.

## Slide 11
        Questions?
https://www.transportation.gov/content/safety-band